## Slide 1
NETWORK DESIGN &
ARCHITECTURE
BIT2154 | Assignment 2
Logical Network Architecture Design & Implementation
January 2026 Semester
Name : Takrim Noor Hamim
Student ID: SUKD2501817
Faculty of Engineering, Built Environment and Information Technology
Bachelor of Information Technology (Hons) | SEGi University

## Slide 2
01. INTRODUCTION
Purpose & Overview

## Slide 3
Introduction
Overview
BIT2154 | Network Design & Architecture | Assignment 2
About This Assignment
This assignment (Assignment 2) implements the physical network design from Assignment 1 (although I changed the design a little bit in packet tracer) into a fully functional logical network using Cisco Packet Tracer. The network consists of three branches (A, B, C) interconnected via serial WAN links, with each branch configured with VLANs, inter-VLAN routing, RIP v2 routing protocol, wireless access, and comprehensive security measures.
Don’t get confused by seeing the names of the router or switch in the configuration just see the headings of those cause I changes some names after the configuration.
Key Objectives
IP Addressing & Subnetting
Assign unique subnets per VLAN per branch VLAN Configuration
VLAN 10 (PCs), VLAN 20 (Server), VLAN 30 (Wi-Fi) Inter-VLAN Routing
Router-on-a-Stick (dot1Q subinterfaces) RIP Version 2
Dynamic routing between all 3 branches Security
Router passwords, banner, port security, unused port shutdown

## Slide 4
02. NETWORK TOPOLOGY
Overall Logical Network Diagram

## Slide 5
Overall Network Topology — Cisco Packet Tracer
Topology
BIT2154 | Network Design & Architecture | Assignment 2
Full network topology showing Branch A , B, C connected via WAN serial links.

## Slide 6
IP Addressing Scheme
IP Config
BIT2154 | Network Design & Architecture | Assignment 2
Subnetting Plan — Per Branch, Per VLAN
Branch | VLAN | Purpose | Network Address | Subnet Mask | Gateway (Router)
Branch A | VLAN 10 | PCs | 192.168.10.0/26 | 255.255.255.192 | 192.168.10.1
Branch A | VLAN 20 | Server | 192.168.10.64/27 | 255.255.255.224 | 192.168.10.65
Branch A | VLAN 30 | Wi-Fi | 192.168.10.96/27 | 255.255.255.224 | 192.168.10.97
Branch B | VLAN 10 | PCs | 192.168.20.0/26 | 255.255.255.192 | 192.168.20.1
Branch B | VLAN 20 | Server | 192.168.20.64/27 | 255.255.255.224 | 192.168.20.65
Branch B | VLAN 30 | Wi-Fi | 192.168.20.96/27 | 255.255.255.224 | 192.168.20.97
Branch C | VLAN 10 | PCs | 192.168.30.0/26 | 255.255.255.192 | 192.168.30.1
Branch C | VLAN 20 | Server | 192.168.30.64/27 | 255.255.255.224 | 192.168.30.65
Branch C | VLAN 30 | Wi-Fi | 192.168.30.96/27 | 255.255.255.224 | 192.168.30.97
WAN A↔B | — | WAN Link | 10.1.2.0/30 | 255.255.255.252 | 10.1.2.1 / 10.1.2.2
WAN A↔C | — | WAN Link | 10.1.1.0/30 | 255.255.255.252 | 10.1.1.1 / 10.1.1.2
WAN B↔C | — | WAN Link | 10.1.3.0/30 | 255.255.255.252 | 10.1.3.1 / 10.1.3.2

## Slide 7
03. BRANCH A
Tree Topology (Star and Bus)

## Slide 8
Branch A — Network Topology (Tree – Star and Bus)
Branch A
BIT2154 | Network Design & Architecture | Assignment 2

## Slide 9
Branch A — Switch VLAN & Trunk Configuration
Branch A
BIT2154 | Network Design & Architecture | Assignment 2
Main Switch (Switch0) — VLANs 10/20/30 created; fa0/1 & fa4/1 set as trunk;
fa3/1=VLAN10 (Bus topology’s line); fa1/1=VLAN30
Star Switch (Switch2) — fa4/1 as trunk; fa0/1=VLAN20; fa1/1, fa2/1, fa3/1=VLAN10

## Slide 10
Branch A — Router Inter-VLAN & RIP v2 Configuration
Branch A
BIT2154 | Network Design & Architecture | Assignment 2
Router1 — fa0/0 subinterfaces: VLAN10=192.168.10.1, VLAN20=192.168.10.65, VLAN30=192.168.10.97
Router1 — RIP v2 configured: networks 10.0.0.0 & 192.168.10.0, no auto-summary, serial WAN IPs assigned.

## Slide 11
Branch A — Port Security & Unused Port Shutdown
Branch A
BIT2154 | Network Design & Architecture | Assignment 2
Port security: max MAC=1, violation=restrict, sticky MAC on fa1/1, fa3/1
Unused ports (fa2/1, fa5/1) shut down to prevent unauthorized access

## Slide 12
Branch A — Router Security Configuration
Branch A
BIT2154 | Network Design & Architecture | Assignment 2
Router1 security: enable secret, console password, VTY (telnet) password (cisco123), banner MOTD, service password-encryption all configured.

## Slide 13
04. BRANCH B
Hybrid Topology (Mesh and Star)

## Slide 14
Branch B — Network Topology (Hybrid – Mesh and Star)
Branch B
BIT2154 | Network Design & Architecture | Assignment 2
Also Did the same
configurations for
Branch B

## Slide 15
Branch B — Switch VLAN & Trunk Configuration (Main & Top Mesh Switches)
BIT2154 | Network Design & Architecture | Assignment 2
Main Switch (Switch3) — VLANs 10/20/30 created; fa0/1 & fa1/1 trunk;
fa2/1=VLAN30 (Access Point); fa3/1, fa6/1=VLAN10
Top Mesh Switch (Switch4) — fa0/1, fa1/1, fa2/1 all set as trunk ports (mesh interconnects)

## Slide 16
Branch B — Switch VLAN & Trunk Configuration (Left & Right Mesh Switches)
BIT2154 | Network Design & Architecture | Assignment 2
Left Mesh Switch (Switch5) — fa0/1 & fa1/1 trunk;
fa2/1=VLAN20 (Server); fa3/1, fa6/1=VLAN10
Right Mesh Switch (Switch6) — fa0/1 & fa1/1 trunk; fa2/1, fa3/1, fa6/1, fa7/1=VLAN10

## Slide 17
Branch B — Router Inter-VLAN & RIP v2 Configuration
Branch B
BIT2154 | Network Design & Architecture | Assignment 2
Router2 — fa0/0 subinterfaces: VLAN10=192.168.20.1, VLAN20=192.168.20.65, VLAN30=192.168.20.97
Router2 — RIP v2: networks 10.0.0.0 & 192.168.20.0, serial3/0=10.1.1.2, serial2/0=10.1.3.1

## Slide 18
Branch B — Port Security & Unused Port Shutdown
Branch B
BIT2154 | Network Design & Architecture | Assignment 2
✅ What Was Done
Same port security configuration applied as Branch A:
• switchport mode access
• switchport port-security
• port-security maximum 1
• violation restrict
• mac-address sticky
• Unused ports shut down
⚠️ Problem Encountered
Initially, port security was accidentally applied to trunk ports also. This caused ping failures between VLANs as trunk ports should not have port-security. The fix was to remove port-security from trunk ports and apply it only to access ports.
📷 Note
Screenshot of the corrected configuration was not captured at the time of fixing.
Missing
Screenshot

## Slide 19
Branch B — Router Security Configuration
Branch B
BIT2154 | Network Design & Architecture | Assignment 2
Router2 security: enable secret, console password, VTY password (cisco123), banner MOTD 'Unauthorized Access is Prohibited!', service password-encryption.

## Slide 20
05. BRANCH C
Hybrid Topology – Bus and Ring

## Slide 21
Branch C — Network Topology (Ring)
Branch C
BIT2154 | Network Design & Architecture | Assignment 2
Also Did the
configurations for
Branch C
(Same way)

## Slide 22
Branch C — Switch VLAN & Trunk Configuration
Branch C
BIT2154 | Network Design & Architecture | Assignment 2
Main Switch (Switch7/9) — VLANs 10/20/30 created; fa0/1 trunk;
fa3/1=VLAN20 (Server); fa0/1, fa1/1=VLAN10; fa6/1=VLAN30
Top Ring Switch — fa2/1 trunk; fa3/1=VLAN20 (Server); fa0/1, fa1/1=VLAN10 PCs

## Slide 23
Branch C — Router Inter-VLAN & RIP v2 Configuration
Branch C
BIT2154 | Network Design & Architecture | Assignment 2
Router3 — fa0/0 subinterfaces: VLAN10=192.168.30.1,
VLAN20=192.168.30.65, VLAN30=192.168.30.97
Router3 — RIP v2: networks 10.0.0.0 & 192.168.30.0, serial2/0=10.1.2.2, serial3/0=10.1.3.2

## Slide 24
Branch C — Port Security & Unused Port Shutdown
Branch C
BIT2154 | Network Design & Architecture | Assignment 2
✅ What Was Done
Same port security configuration applied as Branch A:
• switchport mode access
• switchport port-security
• port-security maximum 1
• violation restrict
• mac-address sticky
• Unused ports shut down
⚠️ Problem Encountered
Initially, port security was accidentally applied to trunk ports also. This caused ping failures between VLANs as trunk ports should not have port-security. The fix was to remove port-security from trunk ports and apply it only to access ports.
📷 Note
Screenshot of the corrected configuration was not captured at the time of fixing.
Missing
Screenshot

## Slide 25
Branch C — Router Security Configuration
Branch C
BIT2154 | Network Design & Architecture | Assignment 2
Router3 security: enable secret, console password, VTY password (cisco123), banner MOTD 'Unauthorized Access is Prohibited!', service password-encryption.

## Slide 26
06. SECURITY CONFIGURATION
Router & Switch Security

## Slide 27
Security — Router Running Config (Part 1 & 2)
Security
BIT2154 | Network Design & Architecture | Assignment 2
service password-encryption enabled; enable secret stored as MD5 hash (Type 5)
Subinterface IPs, serial WAN IPs, RIP v2 configuration confirmed in running-config

## Slide 28
Security — Router Running Config (Part 3)
Security
BIT2154 | Network Design & Architecture | Assignment 2
Banner MOTD: 'Unauthorized Access is Prohibited!'; line con 0 & line vty 0 4 passwords encrypted (Type 7); login required.

## Slide 29
Security — Switch Port Security on a Random Switch
Security
BIT2154 | Network Design & Architecture | Assignment 2
show port-security: MaxSecureAddr=1, SecurityViolation=Restrict on Fa0/1, Fa1/1, Fa2/1, Fa3/1. Sticky MAC learning active.

## Slide 30
07. TESTING & VERIFICATION
Ping Tests, Routing Tables & VLAN Tables

## Slide 31
Testing — Inter-Branch Ping (Branch A → B & A → C)
Testing
BIT2154 | Network Design & Architecture | Assignment 2
✅ Router1 (Branch A) → Router2 (Branch B): ICMP Successful
✅ Router1 (Branch A) → Router3 (Branch C): ICMP Successful

## Slide 32
Testing — Inter-Branch Ping (Branch B → C)
Testing
BIT2154 | Network Design & Architecture | Assignment 2
✅ Router2 (Branch B) → Router3 (Branch C): ICMP Successful — All 3 branches fully interconnected via RIP v2.

## Slide 33
Testing — Inter-VLAN: Branch A (PC → Server & PC → Wireless)
Testing
BIT2154 | Network Design & Architecture | Assignment 2
✅ Branch A: PC7 (VLAN 10) → Server0 (VLAN 20): Successful — Inter-VLAN routing working
✅ Branch A: PC1 (VLAN 10) → Tablet PC0 (VLAN 30): Successful — Wi-Fi VLAN reachable

## Slide 34
Testing — Inter-VLAN: Branch B (PC → Server & PC → Wireless)
Testing
BIT2154 | Network Design & Architecture | Assignment 2
✅ Branch B: PC15 (VLAN 10) → Server2 (VLAN 20): Successful
✅ Branch B: PC11 (VLAN 10) → Smartphone1 (VLAN 30): Successful

## Slide 35
Testing — Inter-VLAN: Branch C (PC → Server & PC → Wireless)
Testing
BIT2154 | Network Design & Architecture | Assignment 2
✅ Branch C: PC7(1) (VLAN 10) → Server1 (VLAN 20): Successful
✅ Branch C: PC21 (VLAN 10) → Laptop2 (VLAN 30): Successful

## Slide 36
Testing — Routing Table: Branch A (Router1)
Testing
BIT2154 | Network Design & Architecture | Assignment 2
Router1: C=directly connected (own VLANs + WAN); R=RIP routes to Branch B (192.168.20.x) & C (192.168.30.x) via serial links
Router2: C=directly connected (own VLANs + WAN); R=RIP routes to Branch A (192.168.10.x) & C (192.168.30.x)

## Slide 37
Testing — Routing Table: Branch C (Router3)
Testing
BIT2154 | Network Design & Architecture | Assignment 2
Router3: C=directly connected (192.168.30.x VLANs + WAN links); R=RIP learned routes to Branch A (192.168.10.x) & Branch B (192.168.20.x).

## Slide 38
Testing — VLAN Table: Branch A & Branch B Main Switches
Testing
BIT2154 | Network Design & Architecture | Assignment 2
Branch A Main Switch: VLAN 10 (fa3/1), VLAN 30 (fa1/1) active; fa0/1 & fa4/1 as trunk
Branch B Main Switch: VLAN 10, 20, 30 created; fa2/1=VLAN30 (Access Point) active

## Slide 39
Testing — VLAN Table: Branch C Main Switch
Testing
BIT2154 | Network Design & Architecture | Assignment 2
Branch C Main Switch: VLAN 10 (fa3/1 active), VLAN 20, VLAN 30 (fa6/1 active) all confirmed present. Trunk ports correctly configured.

## Slide 40
08. CONCLUSION
Summary & Reflection

## Slide 41
Conclusion
Summary
BIT2154 | Network Design & Architecture | Assignment 2
Findings
✅ All three branches successfully implemented in Cisco PT ✅ VLAN 10/20/30 correctly segmenting PCs, Servers, and Wi-Fi users ✅ Inter-VLAN routing via Router-on-a-Stick (dot1Q) working across all branches ✅ RIP Version 2 enabling full inter-branch connectivity ✅ Security measures applied: encrypted passwords, banner, port security, unused port shutdown
Reflection
This assignment deepened understanding of real-world network implementation. Key lessons learned: Subnetting requires careful planning to avoid overlapping networks across VLANs and branches. Trunk vs Access ports — misconfigurations (Native VLAN mismatch) cause connectivity issues and must be resolved. RIP v2 with no auto-summary is essential for classless routing in a multi-subnet environment. Security is not optional — even basic configurations like port security and password encryption significantly harden the network.

## Slide 42
Thank You
Network Design & Architecture | BIT2154 | Assignment 2
January 2026 Semester | SEGi University